## Slide 1: Demystifying T1-MRI to FDG18-PET Image Translation via Representational Similarity
Chia-Hsiang Kao, Yong-Sheng Chen, Li-Fen Chen, and Wei-Chen Chiu
National Yang Ming Chiao Tung University, Taiwan

## Slide 2: Take home message
We use representational similarity to verify our proposed hypotheses that the translation from T1-MR to PET images comprises the recognition of brain tissue types and brain regions.

## Slide 3: Introduction There is a growing research trend in using AI for cross-modality medical image translation.
T1-weighted Magnetic resonance imaging
(T1-MRI)
FDG18-positron emission tomography
(PET)
Nie, D. (2017), Pan, Y. (2018),
Sikka, A. (2018), Sun, H. (2019), Lan, H. (2020)
DL-based image synthesis/translation
Principle | MRI uses strong magnetic fields to identify the anatomical structure of the brain. |  | PET measures the glucose update ability of tissue to quantify the metabolic process.
Drawback | time consuming, high cost |  | injection of radioactive tracer, high cost

## Slide 4: Introduction There is a growing research trend in using AI for cross-modality medical image translation.
Conventional
Latest

## Slide 5: Introduction There is a growing research trend in using AI for cross-modality medical image translation.
Synthetic images are meaningful for subjects in both extremes of disease spectrum.
Left: CN. Middle: MCI. Right: AD. The generated PET images show consistency of hypometabolism (less red, more yellow) with the ground truth image.

## Slide 6: Introduction However, there are several major concerns when it comes to clinical applications.
Robustness to distributional biases (population, organs, diseases).
Robustness to systemic biases (scanning devices and protocols, preprocessing techniques).
Robustness to out-of-distribution cases, noise and adversarial perturbations.

## Slide 7: Introduction Even more, deep learning models remain black-box for most AI scientists.

## Slide 8: Motivation How do deep learning models translate T1-MRI images to FDG-PET images?
?
?

## Slide 9: Motivation How do deep learning models translate T1-MRI images to FDG-PET images?

## Slide 10: Literature Deep learning has been deployed for brain tissue segmentation and brain region identification.
Chen, H., Dou, Q., Yu, L., Qin, J., & Heng, P. A. (2018). VoxResNet: Deep voxelwise residual networks for brain segmentation from 3D MR images. NeuroImage, 170, 446-455.
The example results of validation data (yellow, green, and red colors represent the WM, GM, and CSF, respectively): (a) original MR images, (b) results of VoxResNet, (c) results of Autocontext VoxResNet, (d) ground truth label.

## Slide 11: Literature Deep learning has been deployed for brain tissue segmentation and brain region identification.
Moeskops, P., de Bresser, J., Kuijf, H. J., Mendrik, A. M., Biessels, G. J., Pluim, J. P., & Išgum, I. (2018). Evaluation of a deep learning approach for the segmentation of brain tissues and white matter hyperintensities of presumed vascular origin in MRI. NeuroImage: Clinical, 17, 251-262.
Example segmentation for one of the test images from the MRBrainS13 challenge, trained using the 5 training images available within MRBrainS13.
From left to right: T1-weighted image, T2-weighted FLAIR image, T1-weighted IR image, reference segmentation and automatic segmentation.

## Slide 12: Literature Deep learning has been deployed for brain tissue segmentation and brain region identification.
Iqbal, A., Khan, R., & Karayannis, T. (2019). Developing a brain atlas through deep learning. Nature Machine Intelligence, 1(6), 277-287.
Left: Randomly selected human brain MR scans are shown. Middle: Ground-truth masks of the corresponding MR scans in (a). Right: Outputs of our proposed deep learning models.

## Slide 13: Literature Deep learning has been deployed for brain tissue segmentation and brain region identification.
Tan, C., Guan, Y., Feng, Z., Ni, H., Zhang, Z., Wang, Z., ... & Li, A. (2020). DeepBrainSeg: Automated brain region segmentation for micro-optical images with a convolutional neural network. Frontiers in neuroscience, 14, 179.

## Slide 14: Hypothesis Deep learning models learn to segment brain tissue types.
Align brain images from both T1-MRI and FDG-PET.
Use the value from T1-MRI as and that from FDG-PET as to obtain pairs.

## Slide 15: Hypothesis Deep learning models learn to segment brain tissue types.

## Slide 16: Hypothesis Deep learning models learn to segment brain tissue types.
The gray matter (GM) mainly comprises the neuronal body, which consumes glucose. Thus, GM is white on FDG-PET imaging.
The white matter (WM) mainly comprises the axon, which does not consume glucose. Thus, WM is black on FDG-PET imaging.
Partial volume effect

## Slide 17: Hypothesis Deep learning models learn to segment brain tissue types.
The gray matter (GM) mainly comprises the neuronal body, which consumes glucose. Thus, GM is white on FDG-PET imaging.

## Slide 18: Hypothesis Deep learning models learn to segment brain tissue types.
The gray matter (GM) mainly comprises the neuronal body, which consumes glucose. Thus, GM is white on FDG-PET imaging.
The white matter (WM) mainly comprises the axon, which does not consume glucose. Thus, WM is black on FDG-PET imaging.

## Slide 19: Hypothesis Deep learning models learn to segment brain tissue types.
The gray matter (GM) mainly comprises the neuronal body, which consumes glucose. Thus, GM is white on FDG-PET imaging.
The white matter (WM) mainly comprises the axon, which does not consume glucose. Thus, WM is black on FDG-PET imaging.
Partial volume effect

## Slide 20: Hypothesis Deep learning models learn to segment brain tissue types.
The gray matter (GM) mainly comprises the neuronal body, which consumes glucose. Thus, GM is white on FDG-PET imaging.
The white matter (WM) mainly comprises the axon, which does not consume glucose. Thus, WM is black on FDG-PET imaging.
Partial volume effect
Hypothesis: Deep learning models learn to segment brain tissue types.

## Slide 21: Method d
Dataset
Obtain 1300+ MRI-PET paired data from Alzheimer's Disease Neuroimaging Initiative (ADNI), composed of brain images from cognitive normal people and patients with mild cognitive impairment or Alzheimer’s disease. (International, multi-center, multi-scanning protocols, standard preprocessing procedures)
Preprocess data according to the standard method with SPM software.
Deep learning model
Adopt a widely-used 2D Unet model for MRI-to-PET image translation, which comprises several nonlinear transformation functions .
Goal
Measure and quantify the information of “brain tissue type” along the data transformation process.

## Slide 22: Method d
Black-box transformation process

## Slide 23: Method d

## Slide 24: Method d
Similarity between GM and transformed data
15%
19%
65%
85%
89%
85%
Similarity between WM and transformed data

## Slide 25: Method d
Similarity between GM and transformed data
15%
19%
65%
85%
89%
85%
Similarity between WM and transformed data
We can also compute the similarity between MRI (or PET) and the transformed data.

## Slide 26: Results Brain tissues are segmented in the early encoding stage of image translation.

## Slide 27: Results Brain tissues are segmented in the early encoding stage of image translation.

## Slide 28: Results Brain tissues are segmented in the early encoding stage of image translation.

## Slide 29: Results Brain tissues are segmented in the early encoding stage of image translation.

## Slide 30: Hypothesis Deep learning models learn to segment brain regions.
Normal higher uptake regions
Least altered regions during aging
Regions of hypometabolism in AD
Brain: normal variations and benign findings in fluorodeoxyglucose-PET/computed tomography imaging. (PET Clin. 2014)
Voxel-based mapping of brain gray matter volume and glucose metabolism profiles in normal aging. (Neurobiology of Aging. 2007)
Brain PET in the diagnosis of Alzheimer's disease. (Clin Nucl Med. 2014)

## Slide 31: Results Brain regions are identified in the decoding stage of translation.

## Slide 32: Limitation ff
Dataset – organs, diseases, modalities (e.g., different radioactive tracers), machines.
Models – various deep learning models.
Measurement of similarity – curse of dimensionality.

## Slide 33: Take home message
We use representational similarity to verify our proposed hypotheses that the translation from T1-MR to PET images comprises the recognition of brain tissue types and brain regions.